## Slide 1: Field Gateway Architecture
01-13-2013

## Slide 2: Watchdog slide
RECORD THIS PRESENTATION!

## Slide 3: Content
FGW bird’s eye view
What’s a message?
What’s a module?
What’s a bus?
PRO/CONs
Future directions
Q&A

## Slide 4
Field Gateway
BUS
MODULE1
MODULE2
MODULE3
SENSOR
SENSOR
SENSOR
CAN
232
BLE
MSG
MSG
MODULE4
MODULE5
MSG
IOT
Bird’s eye view
MSG
MSG

## Slide 5: What’s a message?
Atomic piece of data exchanged on the bus
Produced by a module; consumed by 1…n modules
Has
  Properties (“name”:”value”, like JSON, might include “contentType”:”something” to give meaning to byte[])
  Content (byte[])
It is immutable => zero copy operation (just inc_ref/dec_ref)
APIs: _Create, _Destroy, _Clone, _GetContent, _GetProperties

## Slide 6: What’s a module?
Participant at the data exchange on the bus.
APIs: _Create, _Destroy, _Receive
  _Create(BUS_HANDLE, config)
  _Receive(MESSAGE_HANDLE)
  Uses Bus_Publish (BUS_HANDLE, MESSAGE_HANDLE) to send messages
  _Destroy frees system resources
Examples: “says dude”, “says sweet”, “BLE”, “mapping”, “iothubhttp”

## Slide 7: Modules in depth
Different “linkage” levels of modules in the gateway
  Level 0: statically linked. Object is linked in the executable.
    PROs: straight forward
    CONs: no isolation (bad code crashes the whole FGW). Code needs to written in C/C++ as long as it links. Can work on very restricted OSes.
  Level 1: dynamically linked
    PROs: straight forward, distributable as binary, loadable/skippable, can we written in any language that produces .dlls/.so/.dylibs (C/C++, C#, Java*, Visual Basic* etc)
    CONs: no isolation (bad code crashes the whole FGW). Not all OS have dyn loadable libs
  Level 2: process hosted (future)
    PROs: can be binary, loadable/skippable, process isolation, can be written in any language including interpreted!
    CONs: needs IPC (slower, resource usage etc), needs OS which is process capable.
  Level 3: machine/container hosted (future)
    PROs: best isolation - if the whole machine goes down, FGW survives
    CONs: needs RPC…

## Slide 8: What is BUS?
BUS: exchange medium for information, passes MESSAGEs from sources to all other modules.
APIs: _Create, _Destroy, _Publish, _AddModule, _RemoveModule
Performance is paramount:
  bus cannot “block” modules
  bus cannot allow itself to be blocked by modules
Delivers messages in-order, serially

## Slide 9: BUS – MODULE relationship
BUS
MODULE1
MSG3
MSG2
MSG1
Thread
CND
_Receive
MODULE2
MSG3
MSG2
Thread
CND
_Receive
SEPARATION LINE

## Slide 10: FGW pro/con
PROs: great flexibility – allows everything
CONs: great flexibility (data exchange done by convention between modules)
PROs: can do processing pipelines
PROs: BUS is an implementation, can be replaced by other impl
CONs: no delivery guarantees (best effort)
CONs: routing is done at level 7 of OSI stack
PROs: portable with PAL (Windows, Linux support out of the box)
PROs: multilevel FGWs

## Slide 11: Future architecture directions
Protocol translation
Protocol encapsulation
Connection multiplexing
ASSERT(FGW==IOTHUB) module
Internal diagnostics/watchdogs/logs etc
Local cloud services… (ASA, ML etc *cough*)
Provisioning module (?)
DM module(?)
Pipelines
Filtering/targeting/optimizing FGW internal traffic

## Slide 12: Q&A